## Slide 1: Critical Design Review (CDR)
February 10, 2024
SilverSat’s CubeSat and Mission Details
Notes: Green highlight needs to be edited

## Slide 2: Success Criteria for the Review
All Board design changes have been identified for the Flight Model
Flight Software development is well underway and has been tested as part of the Prototype 2 test campaign
Prototype testing demonstrates Level 1 requirements
Mechanical fit check is complete and successful
Slide

## Slide 3: Logistics
Welcome to APL’s B201 Auditorium!
Bathrooms are outside and to the right of the Auditorium double doors
Food is in the back of the room, please help yourself
Please silence your cell phones
For the attendees on the Google Meet, please mute your microphone
The CDR is scheduled to run from 2:30 - 5:30 PM, but there is a lot of material to cover. At ~3:30 PM, we will do a time check to see where we are at in the presentation
Slide

## Slide 4: Overview of SilverSat Limited
Multi-year community-based non-profit serving Silver Spring area tweens and teens
Goals include STEM enrichment “to discover and expand knowledge”* and leadership development among tweens and teens, including those from underrepresented and underserved groups in STEM fields
Diverse student participation -> different perspectives on the different challenges we face throughout this program
  ~15 Students in grades 6-12 as well as in college
  Mix of public, private, and home-schooled students
  Greater Silver Spring area: DC, Maryland, and Virginia
  Many different personal interests and aspirations
* NASA 2018 Strategic Plan, NASA Vision - p.6
Slide
Notes: Zoe

## Slide 5: Outline
Overview & Mission Concept
Systems Engineering
Critical Designs (Major Components)
  Power, Avionics, Radio, Payload, Mechanical, Ground
Prototype 2 Results
Flight Model (FM) Integration and Test Flow
Programmatics
Conclusion/Outbrief
Slide

## Slide 6: Mission Concept
SilverSat is a CubeSat that…
Takes photos of Earth during its orbit and, when in contact with a ground station, logs into X (formerly Twitter) and posts its photos and mission data as posts (formerly Tweets).
Slide
Notes: Aubrey

## Slide 7: Updates Since the Preliminary Design Review (PDR)
Completed designs of printed circuit boards (PCBs)
Finished Prototype 2 testing
Began ordering and receiving Boards and parts for the Flight Model
Implemented, tested, and integrated the Payload, Avionics, and Radio Boards Software
Established and prototyped the Ground Station
Found a new location for building the CubeSat
Established alternatives to X (formerly Twitter)
Slide
Notes: Zoe

## Slide 8: PDR Action Items
Action | Status | Notes
Come up with ideas of how we could use our extra mass margin. | Closed | Team conducted trade study, decided to pursue a backup battery. Ultimately did not incorporate due to heater power.
Find out what other CubeSat missions have used the uCAM camera from 4D Systems. Ask them how well the camera performed, if they had any issues, and what did they do about direct sun illumination. | Closed | Identified five other missions that have used this camera. No additional information on how they avoided direct sunlight. Payload Team met with Dr. Dan Moses for input, and conducted independent assessment of possible Sun damage.
Put together ideas for load shedding. What could our CubeSat do if it needed to turn off loads to save power? Does the EPS already have this function? Decide what if any design changes to make from these ideas. | Open | EPS will shut off bus supplies if Batteries fall below threshold. 5V and 3.3V can be powered down separately.
Try to determine soon what the ground station will be and test it with the AX5043. | Closed | Ground Station Radio is a copy of the CubeSat Radio with external PA, LNA, and switch. Prototype testing conducted with an AX5043 Prototype Board as the Ground Station.
Contact Dave Kubalak concerning ideas for 3-D printing the camera’s lens housing, and about possible lens that are better suited for flight. | Closed | Payload Team contacted Dr. Kubalak after PDR.
Slide

## Slide 9: Concept of Operations
Photo: Take pictures of the Earth from Space
Comms: Communication with Ground Station, automated tweet of photo, status
Sleep: Idle, conserve power, wake for photo or communication, beacon
Photo
Sleep
Comms
Slide
Total: 90 minutes
(1 Orbit)
Notes: Zoe

## Slide 10: CubeSat Block Diagram
Avionics Board
Radio Board
Payload
(Raspberry Pi)
Board
Camera
EnduroSat EPS
Solar Cells
CubeSat Size: 1U
NTE Size: 10cm x 10cm x 11cm
NTE Mass: 1.33kg
Slide
Antenna
Notes: Zoe

## Slide 11: Outline
Overview & Mission Concept
Systems Engineering
Preliminary Designs (Major Components)
  Power, Avionics, Radio, Ground, Payload, Mechanical
Prototype 2 Results
FM Integration and Test
Programmatics
Conclusion/Outbrief
Slide

## Slide 12: Level-2 Requirements
Take a picture of Earth
Shall have a camera
Shall point the camera towards Earth in the northern hemisphere
Shall know when to take a picture
Shall know whether it is stable/not spinning
Shall know if it has enough Battery power to take a picture
Shall implement file management
Slide
Notes: Zoe

## Slide 13: Level-2 Requirements cont.
Post photos and data to X (formerly Twitter)
Shall know when it is able to connect with the Ground Station
Shall tweet
Shall be able to compile information and form it into a text tweet
Shall be able to create a tweet with a photo taken from the file system
Fly in Low Earth Orbit (LEO)
Shall be launched into LEO
Shall conduct the mission from LEO
Shall be able to track the orbit of the CubeSat
Shall be able to know where the CubeSat is at all times
Slide
Notes: Zoe

## Slide 14: Level-2 Requirements cont.
Meet CubeSat Design Specification Requirements:
Shall conform to the CubeSat Design Specification
Shall conform to the Nanoracks Flight Acceptance Test Requirements for Lithium-ion Cells and Battery Packs
Shall conform to the Nanoracks CubeSat Deployer (NRCSD) Interface Definition Document (IDD)
Slide
Notes: Zoe

## Slide 15: Mass Budget
Total CBE: 823 g
Total MEV: 853 g
NTE Mass: 1.3 kg
Average Contingency: 4.6%

## Slide 16: Mass Budget
We have a comfortable margin of 446g or over 50%. The heaviest components (solar panels) have had their final mass measured.
Components | CBE (g) | Contingency | MEV (g) | BOE
Frame | 107.5 | 5% | 112.9 | Measured - Engineering Model
EPS | 238.5 | 5% | 250.5 | Measured - Engineering Model
Radio Board | 40.8 | 5% | 42.8 | Measured - Engineering Model
Payload Board | 69.5 | 5% | 73.0 | Measured - Engineering Model
Avionics Board | 48.6 | 5% | 51.0 | Measured - Engineering Model
Solar Array PCM10A2-R11102201 | 43.0 | 0% | 43.0 | Measured - Flightware
Solar Array PCM10A1-R11102212 | 43.3 | 0% | 43.3 | Measured - Flightware
Solar Array PCM10A1-R11102211 | 44.1 | 0% | 44.1 | Measured - Flightware
Solar Array PCM10A1-R11102213 | 43.4 | 0% | 43.4 | Measured - Flightware
Solar Array & Antenna | 108.6 | 0% | 108.6 | Measured - Flightware
Coax | 6.0 | 5% | 6.3 | Data Sheet
Magnets | 12.0 | 15% | 13.8 | Estimation
Cabling | 18.0 | 15% | 20.7 | Estimation
Total weight: | 823.3 | 4.6% | 853.4 | Measured: 85%
Notes: wip

## Slide 17: Power Board
Slide
Notes: Josh

## Slide 18: CubeSat Block Diagram
Avionics Board
Radio Board
Payload
(Raspberry Pi)
Board
Camera
EnduroSat EPS
Solar Cells
CubeSat Size: 1U
NTE Size: 10cm x 10cm x 11cm
NTE Mass: 1.33kg
Slide
Antenna
Notes: Zoe

## Slide 19: Driving (Derived) Requirements
The Board shall use five solar panels to charge the Batteries during the mission.
The Board shall provide the correct voltage power to the Avionics Board.
The Board shall provide the correct voltage power to the Payload and be able to switch the latter on and off.
The Board shall provide the correct voltage power to the Radio System.
The Board shall be able to give diagnostic reports to the Avionics Board.
The Board shall have a reasonable difference between the amount of power generated by board as compared to the usage of the satellite over a cycle.
The EPS Battery shall be compliant with Nanoracks requirements
for ISS launch.
Slide

## Slide 20: Final Design
The EPS design was halted after consultation with Nanoracks over concerns about Li Ion Battery qualification, and suggested we use a qualified EPS.
We selected the EnduroSat EPS based on lowest overall cost that met or exceeded requirements. Other EPSes considered were GomSpace and Clyde Space.
This EPS has been successfully flown and Nanoracks was familiar with the product and the product was qualified for ISS launch.
Slide

## Slide 21: EnduroSat EPS Board Overview
Key Features
Includes Li Ion Batteries and Battery Heaters, Stores up to 10.2 Watt Hours
Draws current through three independent maximum power point trackers, from diode or’d pairs of solar cell sides.
Outputs at 5 V and 3.3 V with additional and latch up protected outputs (LUP) tripping at 2 Amps
Acceptable input voltage range from solar cells (up to 5.5 V)
Battery voltage typical 3.7 V
All outputs short circuit protected
I2C interface
Slide

## Slide 22: EnduroSat Customized the EPS in These Ways…
Our design requires the EPS to be in the center of the stack. EnduroSat modified the housing and H1/H2 pins to provide a stacking connector.
EnduroSat’s base design does not include Battery inhibits
  They add roller switches, which are hard-wired internally (no connectors)
EnduroSat altered the H1/H2 pinout, adding outputs to pins which were unconnected on earlier designs
  Caused a conflict with our pin assignment
  Made modifications to the prototypes to verify the changes
  The H1/H2 definition will be revised on the flight board designs
Slide

## Slide 23: Power Budget Model
Solar Cells
EPS
3.3V
Regulator
5V
Regulator
Diode
MPP
Battery
Payload
LUP5V
Radio
Avionics
The EPS has multiple internal energy sinks
Each circle represents an energy sink
The margin is the difference between the Input Energy (square) and the sum of the energy sinks (circles)
Slide
Battery Heaters
EPS Processor

## Slide 24: Power Budget Assumptions
Solar panels on only 5 of 6 sides.
We will not attempt a tweet unless a pass is greater than 300 seconds (5 minutes). See graph to right.
Avionics will shut down an active tweet if it takes longer than 600 seconds.
Baseline Assumption*: Input power contributed only from one side at a time But analysis of all Cubesat solar cross-section at angles provides margin.
Antenna can be switched off after it is deployed.
No energy captured from Albedo or other IR radiation sources (Earth).
Beacon time base is 100mS (time to transmit a dit).
Beacon interval is 90 Seconds.
*This simplified assumption is very conservative and we believe we get more power
Slide

## Slide 25: Input Side Baseline Power Budget: Solar Cell Power
Based on 1353 W/m2 insolation,
power with one side illuminated broadside (2-3 sides may be illuminated - total on next slide)
EnduroSat solar cell on 5 sides of the cube
Slide
(1.22 W includes a ⅚ factor for one missing side)

## Slide 26
Power Budget Includes Evaluation of Total Sun the Cubesat Receives at Various Orientations
The amount of sun received depends on the angle of the Cubesat.
  Note that the camera side does not have a solar cell.
One, two, or three sides may be illuminated at any given time.
Total intercepted sunlight by a cube equivalent to that of a cross section of a sphere of equal surface area.
6s² = 4πr² equating sphere and cube area
r² = 3s²/(2π) finding r² of sphere
πr² = π * (3s²/(2π))= 1.5s² cross section of sphere
A = (⅚)*1.5s² = 1.25s² average solar cross section of 5 sided cube
.
Area = 1x
Area = 0
Area = √2 x
Area = ½ √2 x
Area = √3 x
Area = ⅔ √3 x
Six cases and useful illuminated area fraction
Average sun exposure of randomly oriented 5 sided cube is 25% higher than broadside illumination of one side.
Broadside
Edgewise
Cornerwise
With Camera side
Only Solar Cell sides
Slide
Notes: Cade

## Slide 27: Battery Heaters
Heater energy was identified as a risk
We need to estimate the energy needed to run the Battery Heaters
  Final results are pending a full thermal model of the Satellite
Heater energy estimate uses a simplified thermal model for the Satellite and EPS
  We want the Batteries to be at or above 0 C
  We have to supply the equivalent amount of energy is lost during an orbit
  Assume there's an insulation layer around the EPS
    5mm thick layer of cryogel insulation, top/bottom
    EPS is thermally isolated from frame
    Assume conduction from EPS top/bottom to outside through insulation
    Outside temp of Satellite varies between -88 C and +35C (based on equilibrium temps)
    No assumption of Battery to case conduction (i.e. Tcase=Tbattery)
Net loss estimate is about 127 joules
EPS
Insulation
Insulation
Solar panel
Solar panel
Solar panel
Frame
Frame
Rad.
Rad.
Slide

## Slide 28: Power Budget
The budget is based on system states representing a day in the life of the Satellite
  Beacon (beacons only)
  Photo (photo w/ beacons)
  Comms (tweet w/ beacons)
Slide
 | "SLEEP" | "PHOTO" | "COMMS"
 | Beacons Only | Photo w/Beacons | Tweet w/ Beacons
Number of beacons (per orbit) | 61 | 61 | 57
Input Energy | 10119 | 10119 | 10119
Input Diode | 464 | 464 | 464
MPP Charger | 965 | 965 | 965
Net input to battery | 8689 | 8689 | 8689
Heaters | 127 | 127 | 127
EPS | 408 | 408 | 408
Payload | 0 | 342 | 855
Radio (receive) | 1156 | 1156 | 1156
Radio (beacons) | 1392 | 1392 | 1301
Radio (tweet) | 0 | 0 | 883
Avionics | 847 | 847 | 847
Net out of battery | 3930 | 4272 | 5578
watts(OAP) | 0.712 | 0.774 | 1.010
Net Excess Energy | 4759 | 4417 | 3112
MEV Net Excess Energy per Orbit | 3532 | 3121 | 1674
Largest risk remains heaters

## Slide 29: Next Steps
Consider replacement of 3.3V regulation scheme for lower overhead current
Complete measurements of required currents
Verify time taken to tweet/take a photo*
Revise H1/H2 definition pins
*Timeline affects how much energy is needed to tweet
Slide

## Slide 30: Currently Working On? Going into Flight Model Build…
The EnduroSat EPS 3.3V regulator is extremely inefficient at our current level
Considering placing linear 3.3V regulators on Avionics and Radio Boards and regulate down from the raw Battery voltage
Slide

## Slide 31: Avionics Board
Slide

## Slide 32: CubeSat Block Diagram
Avionics Board
Radio Board
Payload
(Raspberry Pi)
Board
Camera
EnduroSat EPS
Solar Cells
CubeSat Size: 1U
NTE Size: 10cm x 10cm x 11cm
NTE Mass: 1.33kg
Slide
Antenna
Notes: Zoe

## Slide 33: Driving (Derived) Requirements
The Avionics Board shall…
Keep track of time using a real time clock
Formulate the beacon message
Determine the time at which the CubeSat should transmit a beacon message
Communicate the beacon message to the Radio Board at the time determined for beacon transmission
Collect and process power measurements from the Power Board
Generate the Power Board beacon character based on Power Board performance measurements
Determine the Avionics beacon character pertaining to the Avionics Board state of health
Receive and process uplink commands via the Radio Board
Be in control of the power state of the Payload Board
Be able to communicate what state the Payload Board shall be in when it beats what.
Be able to acknowledge a received command
Be able to check GPIO shutdown pin
Protect itself from software bricks using the watchdog tick
Give information on the status of the other boards
Give telemetry information.
Slide

## Slide 34
Microcontroller
Samd21
GNC
Adafruit MPU 6050
Real time Clock
DS1337
I2C
I2C
Reset line
Watchdog tick
Watchdog chip TPS3813-Q1
Fram CY15B256J
page
Avionics Diagram - Connections Inside the Board
SN74B3Q3306A I2C Switch
34
74LVC1 Open Drain Buffer x6
SN65HVD70D Serial Drivers x2
GPIO lines
TxD x2
RxD x2
USB Port
USB Line
Notes: Nicholas

## Slide 35
Avionics
To/From Payload
RxD
TxD
Gpio shutdown
Gpio States(Tweet and Picture)
3.3V
To/From Power Board
Payload On
Payload On 0=on 1=off
Shutdown 1=shutdown possible 0=Pb on
States 1=tweet 0=photo
Avionics Diagram - Connections to Other Boards
page
35
I2C
I2C
To/From Radio Board
RxD
TxD
I2C
Notes: Nicholas

## Slide 36: Final Design
The Flight (V2.0) version of the Avionics Board will include
Revised Hardware that complies with New EnduroSat Header Definition.
New Graphics allows for easier identification of Regions on the Board and Other Headers and Test Points.
Original THT LEDs replaced with New SMD LEDs.
Pull Up Resistors added to Open-Drain Buffers.
Slide

## Slide 37: Avionics Board V1.0
The Avionics Board V1.0 was very successful, with no major hardware issues present.
Minor issues did present, for example, the open drain drivers required pullup resistors to prevent Payload from accidentally starting up on boot.
Slide

## Slide 38: Code
Made the first prototype codebase to test the software for different components
Made the second prototype codebase that started to integrate the different parts of the codebase together
Made the third prototype codebase which fully integrated the parts of the codebase
Flight Model will get rid of unnecessary code that was used for testing and try to optimize the code as much as possible
Slide

## Slide 39: Code cont.
Codebase had a few main parts to it
  Code for the different hardware components
    Watchdog timer
    Ds1337 real time clock
    Antenna
    FRAM
    Communications with other CubeSat Boards
    IMU to detect the orientation of the Satellite
  Code for the different commands
  Code for the beaconing
  Code for determining photo time
  Code for controlling Payload
  Code for receiving commands from Radio
Slide

## Slide 40: Prototype 2 Test Results
Avionics Board header pin reassignment tested successfully (no collision issues)
Open-Drain Buffers pull down resistors functioned as expected (Payload did NOT boot up on power on)
Slide

## Slide 41: Currently Working On? Going into Flight Model Build…
Fixing Issues: Header pin assignments changed in response to allow synergy with the EnduroSat EPS. Pull-up resistors connected to open-drain buffers to prevent Payload from booting on power on.
Adding helpful graphics: Drawing boxes around different regions of the Board to help identify circuits and other test points and headers
Replacing LEDs: Non-functioning THT LEDs replaced with SMD LEDs, and resistors replaced to obtain proper voltage drop
Slide

## Slide 42: Radio Board
42
Slide

## Slide 43: CubeSat Block Diagram
Avionics Board
Radio Board
Payload
(Raspberry Pi)
Board
Camera
EnduroSat EPS
Solar Cells
CubeSat Size: 1U
NTE Size: 10cm x 10cm x 11cm
NTE Mass: 1.33kg
Slide
Antenna
Avionics and Payload UARTs pass through H1/H2. The Antenna has a dedicated connector.
Notes: Isaac

## Slide 44: Driving (Derived) Requirements
The Radio Board shall…
✅ provide an Internet connection to and from Avionics Payload
✅ provide basic status for the beacon
✅ tx. beacon and rx beacon info from avionics every one and a half minutes, but no more than 10
✅ transmit a beacon using Morse code every one and a half minutes
✅ receive beacon information from Avionics
✅ receive signals from the ground
✅ transmit signals to the ground
transmit data using AX25.
✅ exchange data with the rest of the CubeSat using KISS
✅ send commands from the ground station to avionics.
✅ receive commands
✅ communicate with Avionics using the KISS protocol
✅ transmit at a frequency near 438 megahertz (operating range 400 to 520 MHz)
✅ receive signals at a frequency near 438 megahertz
❌ transmit with an output power of no less than 30 dBm (28 dBm measured)
✅ transmit signals with a standard data speed of no less than 9600 baud
✅ receive signals with a standard data speed of no less than 9600 baud
exhibit a noise figure of no greater than 2 dB (✅ ground only)
✅ exhibit an implementation loss of no greater than 3 dB
✅ have a mass of no greater than 112.8 grams (40.77 g measured)
✅ consume no more than 2.574 watts while transmitting (2.37 watts measured)
❌ consume no more than 82.5 milliwatts while receiving (90 mW measured)
✅ receive data from the raspberry pi
✅ receive configuration commands
✅ be fast enough to carry a full TCP/IP connection, but still conserve power and bandwidth
44
page
Notes: Isaac

## Slide 45: Link Budget
Slide
Downlink | 
Transmitter Output Power (dBm) | 28.00
Cable Losses (dB) | -0.50
Antenna Gain (dBi) | 0.00
Output EIRP (dBm) | 27.50
Receiver Power (dBm) at 1 570 km (12.09°) | -110.19
Margin (dB) at 1 570 km (8.97°) | 5.78
Required BER = 10-7
Uplink | 
Transmitter Output Power (dBm) | 40.00
Cable Losses (dB) | −1.00
Antenna Gain (dBi) | 15.5
Output EIRP (dBm) | 52.30
Receiver Power (dBm) at 1 570 km (12.09°) | −98.69
Margin (dB) at 1 570 km (8.97°) | 17.28
Notes: Isaac

## Slide 46
Reference: Satellite Radio Block Diagram with Detail
Slide
Proto had no major hardware issues.
Revisions for final will include:
An attenuator was added to the receive path, but it should be on the transmit path
Power amplifier was saturated
Notes: Isaac

## Slide 47
Transmitter
DC block
nooelec LNA
DC block
SilverSat Radio Board
Laptop
The variable attenuator was adjusted to provide between -114 to -128 dBm
Bit Error Rate Testing
(LNA included in the second test)
50.7 dB 60 dB
0 to 30 dB
0 dBm
24 dB gain
Slide
“Cookie tin shielded enclosure”
Shielded box
Notes: Cade

## Slide 48: Bit Error Rate Testing cont.
48
Slide
These are the results
without an LNA.
But how well does our receiver perform?
Given a required Eb/No of 13.3dB @ 10−5 BER (Non-coherent FSK), and using the AX5043 receiver BW (14.4 KHz), the minimum detectable signal should be -119 dBm (0 dB NF).
Our measurements show a 5dB deviation, split between receiver front end noise and implementation losses.
Subsequent measurements with an external LNA showed an improvement between 4 to 5 dB.

## Slide 49: Things We Might Want to Add
Improving Link Margin
  We’re barely getting +28.5dBm right now (should be 30)
    current PAE is roughly 28% (should be closer to 50), but haven’t played with tuning
  Can improve to +32-34 dBm at cost of more DC power draw (at peak output)
    4dB improvement on downlink margin where we’re tightest
    GRF5504 or HMC453 (drop in replacement)
  If PAE numbers are to be believed, this would cost an additional 700 J per tweet
Add an LNA
  The decision is to include the LNA on the ground side, but probably not include the LNA on the satellite
  This isn’t the link that is power limited and more likely to have strong in-band interferers, but there is room in the power budget
  We would need to add/design a front-end filter
  MAX2650, 0.7dB NF, 3.5mA typ @ 3.3V
  Filter for LNA
  SAW based filter, TA1808A, 440MHz, 20MHz BW, 2.4dB IL
  Or design our own ;)
  May want to have a filter regardless due to adjacent channel interference
  Still need to do a proper survey once we have a frequency
Secondary radio
  Adds full duplex and redundancy
  Needs another 435 to 438 MHz frequency; a request AMSAT may not grant
  Potentially include an Iridium SBD module for AMSAT compliance, but that will require an additional Antenna
All items, except beacon characters, require approximately six months to implement. LNA and filter require frequency allocation before they can start.
Slide
Notes: Isaac

## Slide 50: Payload Board
50
Slide

## Slide 51: CubeSat Block Diagram
Avionics Board
Radio Board
Payload
(Raspberry Pi)
Board
Camera
EnduroSat EPS
Solar Cells
CubeSat Size: 1U
NTE Size: 10cm x 10cm x 11cm
NTE Mass: 1.33kg
Slide
Antenna

## Slide 52: Driving (Derived) Requirements
Input/Output
  Board Power switch (Input from Avionics, +5VLUP from Power)
  Photo/Tweet (Input from Avionics)
  Running/Shutdown (Output to Avionics)
  Differential Serial (Input/Output Radio)
Take Photo
  Switch RPi Serial to Camera****
  Use Camera to take photo
  Save photo to filesystem
Send Tweet
  Switch RPi Serial to Radio****
  Set up network, run startup scripts
  Login to Twitter and tweet text or photo if present
  Remove photo if successful
Slide
**** New since PDR
Notes: AlexG

## Slide 53: Payload Board - Connections
Payload
5v
RxD
TxD
GPIO Shutdown
Payload On
To and From Avionics
GPIO States (Tweet and Picture)
From Battery Board
I2C Data SDA
I2C Clock SCLK
Slide
To and From Radio
Notes: AlexG

## Slide 54: Payload Board - Block Diagram
74HC157 (Serial switch)
Radio/ Camera Pin (26)
Tx/Rx
74lVC1
(Open drain buffer)
+5V Power Switch
74lVC1
(Open drain buffer)
74lVC1
(Open drain buffer)
Payload On
+5V Power
+5V
Slide
I2C Data & I2C Clock SCLK
Notes: AlexG

## Slide 55: Payload Board - PCB Layout
Slide
Notes: AlexG

## Slide 56: Payload Board - Schematic
Slide
I2C Bus Switch
Open Drain Buffers
RPi
Headers
Max3100 &
uCAM-III
Transceiver
Side Header
LEDs
Power Switch
Serial Switch
Notes: AlexG

## Slide 57: Payload Board - Software Flowchart
Slide
Notes: AlexG

## Slide 58: Payload Board - Prototype 2
Slide
Notes: AlexG

## Slide 59: Payload Board - Prototype 2
Slide
Serial Switch (Dead Bug)
Side Header
Camera (uCAM-III)
Transceiver
Raspberry Pi
Notes: AlexG

## Slide 60: Payload Board - Software Infrastructure
Configuration system in github for Raspberry Pi (Payload/Ground)
  Simple, reliable, repeatable, named setups for Raspberry Pi
Swappable Python modules for simple switching of components
  Camera connection (SPI/Serial); Twitter post (vs alternatives), etc.
Mini File Server (MiniFS) on Ground for file upload/download to Satellite
  Auxiliary startup script from Ground, logfiles to Ground
Twitter alternatives - Reddit or MiniFS
  MiniFS (on Ground) can be patched, post to multiple sites
  Consistent interface for Satellite regardless of destination
Slide
Notes: AlexG

## Slide 61: Payload Board - Prototype 2 Test Results
Slide
Payload Board demonstrated its ability to:
Avionics signaling
  Correctly powers up when Power On lines high
  Correctly interprets PHOTO/TWEET on States lines
  Correctly sets RUNNING/SHUTDOWN on Shutdown lines
Take a photo
  Sets Serial switch, syncs with camera, saves photo in filesystem, increments photo counter
Establish network connection,
  Sets Serial switch, runs network setup commands, pings the ground, sets the clock, downloads auxiliary startup script, executes code, and sends upload logs to ground
Tweet
  Checks for a photo to tweet, text tweet if no photo, if there is a photo tweet deletes photo
Notes: AlexG

## Slide 62: Payload Board - Prototype 2 Test Results cont.
Current Draw
  Sleep mode: 0 current draw
  RPi on: 200 to 300mA
Running Time
  Bootup: ~50 seconds
  Take photo: ~90 seconds
  Tweet: ~5 minutes
Total Power Usage Estimates
  Photo: 140 Joules
  Tweet: 350 Joules
Slide
Notes: AlexG

## Slide 63: Currently Working On? Going into Flight Model Build…
Redesign of Payload Board PCB for serial switch
Low-power Satellite Raspberry Pi configuration
  Turn off HDMI, WiFI, etc.
Determine total power consumption for photo and tweet modes
  Depends on size/complexity of photo
Easily change tweet text from Ground, and
  Implement tweet text placeholders for Payload status values
Slide
Notes: AlexG

## Slide 64: Ground Station
64
Slide

## Slide 65: Driving (Derived) Requirements
The Ground Station shall...
... transmit and receive Radio signals
The Ground Station's computer shall host the Satellite's Internet connection
... use tracking software to locate the CubeSat
... send and receive commands
... send and receive data in a data format
... receive the Satellite's beacon and status characters
... use the location of where we want the CubeSat to be when we take a picture, predict when it will reach it, and send the picture time to the Satellite
... receive and filter through public requests for a location of the picture
A person, either a licensed Amateur Radio Operator or under the supervision of an Amateur Radio Operator, shall be at the control point
... consist of the components necessary for proper and sufficient operation, including, but not limited to, those found in the Ground Station block diagram
... send a consistent ping up to the CubeSat to start the process of connecting to the CubeSat
65
page
Notes: Isaac

## Slide 66: Ground Station Software
Ground Station Software Establishes Flask Server
Listens and connects with GPredict to get Radio Doppler Frequencies
Provides Interface for Commands
Waits for Input Request/ Submission
Server Converts Data and Sends through Radio
On Input,
Creates/Sends a Request to Server
Decodes and Writes Responses on Interface
Listens for Response Transmissions
Slide
What does it do?
Enables Commands
Display Status
Rapid Entry of Commands
Controls Radio Frequency
Future Tasks
Implement and Test Antenna Control

## Slide 67
Slide

## Slide 68: Big Picture
Ground Station
(inside)
Ground Station
Controller
Local
Network
(to internet)
Ground Station
(outside)
Antenna
Antenna
Positioner
Mounted near Antenna for lowest loss
30 meters?
~ 1 meter
Tx, Rx & Sw.Cntl
Slide
Location: Goddard Amateur Radio Club clubhouse, Glenn Dale, Maryland
HAAT: −15×10⁻¹ m* plus tower height
* United States Federal Communications Commission (2016, January 21). Antenna Height Above Average Terrain (HAAT) Calculator, output for 39°00’42.36‘‘N, 76°50‘21.33˘W. https://transition.fcc.gov/fcc-bin/haat_calculator?dlat=39&mlat=0&slat=... Accessed May 24, 2022 12:00 PM
Notes: isaac

## Slide 69: Ground Station Inside Segment Detail
GS Transceiver PCB (all one board)
AX5043
Differential Match
Single Ended Match
PA
47dBm(min)
Toptek PA-80u
G=13dB(min)
NF = 2.5dB
Driver Amp
Pout 36dBm (min)
G ~ 19dB
Cable LMR600
100 ft. ~ 1.7dB
2x SMA
SAMD21
Pi attached by 40 Pin header:
Serial, 5V (to Pi), 3V3 (from Pi), optional GPIO
Alternative: RPi 4 or 5 attached via ribbon cable
Cable LMR600
100 ft. ~ 1.7dB
2x SMA
GROUND
PC
RPi
Zero 2 W
Cable
Power Supply
13.8V 15A min
FTDI
FT232RNL
USB
Type B
or Micro
SMA
SMA
13.8V
Switch control (5x AC gate driver)
F
To
Outside Switch
X mm
Plug
RPi Zero 3V3 can source 500mA
13.8VDC to 5VDC
USB
Micro
Debug Port
Cable
RG59
100 ft.
2x F
Slide
Antenna Controller
RT-21 AzEL
115VAC -3A
230VAC - 1.5A
To Antenna Rotator
Notes: Miguel, Isaac
The yellow block is the main radio transceiver and interface for the ground station.
It is based on the Satellite radio board, except that the space specific parts have been removed.
The RF output switch was also removed, and has been replaced with separate receive and transmit connectors.
The board can optionally integrate a raspberry pi, that talks to Twitter

## Slide 70: Indoor Ground Station Mechanical Design
Slide
4U, 13″ Deep Molded Audio Rack
G-PRO-4U-13
48.26 x 34.29 x 18.29 cm
Indoor Ground Station CAD Model
GS Transceiver PCB
Antenna Controller
Power Supply
Power Amp
Driver Amp
Indoor Box: Compact, easy to transport, provides enough space for circulation
Notes: Aidan

## Slide 71: Top-Level Diagram (Outside Segment)
Cable
10 ft ~ 0.2dB
2x N
LMR600
Antenna
M² 436CP16
13.3dBi gain
LNA
0.4dB NF,
G=18dB
IP3 +39.7dBm
Pin, max = 21dBm (mini-circuits)
Switch
IL=1dB(max)
Pin = 46dBm(max)
ISO = 31dB (min)
FILTER
IL=0.15dB
430-440MHz
FILTER
IL=0.15dB
430-440MHz
Cable
0.1m ~ 0.14dB
2x SMA
LMR100
Cable
0.1m ~ 0.14dB
2x SMA
Cable
0.1m ~ 0.14dB
2x SMA
LMR100
5V, 95mA
12-15V, 250mA
Switch control
F connector
From Transceiver
N
N
From PA
To Transceiver
Bias Tee
13.8V to 5V
5V, 40mA
Slide
Notes: isaac

## Slide 72: Outdoor Ground Station Mechanical Design
Slide
WH-22-03 Hinged Nema Enclosure
34.9 x 24.9 x 14.9 cm
LNA
Switch
Filters
Outdoor Box: Waterproof, components are easily accessible
DC Converter
Outdoor Ground Station CAD Model
Notes: Aidan

## Slide 73: Activities Since PDR
Added more licensed operators: we have 5 Students and 3 Mentors with licenses. Two more Students and 1 Mentor plan to take the exam in February
Obtained Club Call sign: KC3VVW*
Submitted AMSAT coordination request
Slide
* United States Federal Communications Commission (2023). ULS License: Amateur License - KC3VVW - Silversat. https://wireless2.fcc.gov/UlsApp/UlsSearch/license.jsp?licKey=4748227 Accessed 29 January 2024.
Notes: Isaac

## Slide 74: Currently Working On? Going into Flight Model Build…
Radio Board: Our ground transceiver
Finalizing the Indoor and Outdoor Ground Station Mechanical Design
Slide
Notes: Isaac

## Slide 75: Beacon Box
The goal is to have an all-in-one,* easy use portable beacon receiver.
The Beacon Box will be used to receive status updates from the Satellite.
With an max budget of $150 and made out of easily accessible parts, it’s the perfect educational project. It's a great demo tool that is both cheap and portable. Allowing people to hear a Satellite in space put up by Students just like them.
*Antenna has to be added
Requirements: External Antenna connect CW mode Min range of 420-440 MHz Output Demodulated audio
Goals: CW signal to plain text Receive frequency over USB or IP (used with gpredict) Easily repairable and plug in programmable Full documentation Portable

## Slide 76: Beacon Box
The software will be created in Python using GNU Radio Companion and PyEphem it will be running on an SDR and Raspberry PI.
Notes: wip

## Slide 77: Mechanical
Slide

## Slide 78: CubeSat Model
The CubeSat is a 1U design that is 10 cm x 10 cm x 11 cm and 1.33 kg max
The CubeSat design consists of the following components
  Frame
  Board Stack
  Antenna
  Solar Cells
The CubeSat design will meet the mechanical requirements outlined in the following specifications
  CubeSat Design Specification (CDS Rev 13)
  Launch Services Program Requirements Document (LSP-REQ-317.01 B)
  Nanoracks CubeSat Deployer Interface Control Document (NR-NRCSD-S0003)
  Launch Vehicle Requirements Document (TBD)
Slide
Notes: Anthony

## Slide 79: CubeSat Model
Frame
X/Y Solar Cell (4X)
-Z Solar Cell
Antenna
+Z Closeout Panel
Board Stack
Camera
(mounted to Payload Board)
+Z
Slide
Roller Kill Switches (3X)

## Slide 80: CubeSat Frame
Purchased from EnduroSat
Open frame, multi-piece construction design
Has flight heritage
Material: Aluminum
Finish: Hard anodized surface
Mass: 120g
Threaded Brass Rod (4x)
Separation Spring (2x)
+Z Plate
-Z Plate
Side Rails (4x)
Slide

## Slide 81: Board Stack
Slide
Electrical Power System (EPS1)
(Provides power to the CubeSat)
Radio Board
Payload Board
(Has the camera and Raspberry pi)
Avionics Board
(Board has a hole for the camera)
Aluminum Standoff (16x)

## Slide 82: Currently Working On? Going into Flight Model Build…
Setting up the Prototype and fixing problems that may arise
Finalizing and purchasing the +Z closeout panel
Slide

## Slide 83: Prototype 2 Results
Slide

## Slide 84: Prototype 2 Process (Fit Check)
Assembled the CubeSat to ensure each component could fit and the standoffs were correct
Slide

## Slide 85: Prototype 2 Process (FlatSat)
Designed and wired the FlatSat Board in KiCAD and Creo so that other Teams could test
Slide
Creo CAD Model
KiCad PCB Layout

## Slide 86: What We Learned from Prototype 2
The release switch for the CubeSat was rubbing against the side of the frame, making it so the switch couldn’t spring back
The standoffs weren’t right the right size and couldn’t be screwed on, so we switched to non-threaded standoffs
Slide

## Slide 87: FlatSat Testing
Long PCB board with connected headers for Radio, Battery, Payload, and Avionics side by side.
Also prototype Ground Station components with Radio Board, Raspberry Pi, and laptop for sending commands
Radios connected with a cable
External Radio for listening to beacon (morse code) and communication between Satellite and ground
Slide
Notes: Noah

## Slide 88: FlatSat Testing - Day in the Life
Day in the Life is the things we will do most days when we are in space
The big commands the Satellite will do are…
  Set the Avionics real-time clock (once)
  Turn on Payload for communication (Tweet)
  Register a specific time for Payload to take a photo (Payload turns on at the correct time and takes a photo)
  Turn on Payload for communication (Tweet w/ photo)
We tested the FlatSat to find out how long it took to tweet text, tweet different sizes of images, and take a picture
There are four pieces of data sent between the Satellite, the Ground Station, and Twitter; Auxup, Logsdown, Tweetdown, and Tweetup
Slide
Notes: Charlotte

## Slide 89: FlatSat - Tweet Amount
Bytes
Slide
Notes: Charlotte

## Slide 90: FlatSat - Tweet Times
Slide
Notes: Charlotte

## Slide 91: Outline
Overview & Mission Concept
Systems Engineering
Critical Designs (Major Components)
  Power, Avionics, Radio, Ground, Payload, Mechanical
Prototype 2 Results
FM Integration and Test
Programmatics
Conclusion/Outbrief
Slide

## Slide 92: Flight Model Build Plan
Slide
Fab Bare Avionics Board
Fab Bare Radio Board
Fab Bare Payload Board
Populate Avionics Board
Guidance and Control Board
Microcontroller Circuit Card
Real-Time Clock Connectors
Populate Radio Board
Receiver
Beacon
Populate Payload Board
Raspberry Pi Zero
Camera
Connectors
Fab +Z closeout panel
Purchase frame
Purchase EPS1 Module
FlatSat Test
Assemble board stack onto base plate
Install top plate and rails
Install solar panels, Antenna, and +Z closeout panel
Assembly complete
Purchase Antenna
Purchase solar panels
Notes: Aidan

## Slide 93: Flight Model Test Plan
Day In The Life (DITL) Test
Deliver to Nanoracks
Vibration Test
Comprehensive Performance Test
Comprehensive Performance Test
From Previous Slide “Build Plan”
Slide
*Optional
Thermal Vacuum Bakeout (TVAC) Test*
Go for Launch!!!

## Slide 94: Outline
Overview & Mission Concept
Systems Engineering
Critical Designs (Major Components)
  Power, Avionics, Radio, Ground, Payload, Mechanical
Prototype 2 Results
FM Integration and Test
Programmatics
Conclusion/Outbrief
Slide

## Slide 95: Risk Matrix
Risk # | Risk |  |  |  |  |  |  | L | C
1 | If critical personnel leave the team, then our critical path will be affected |  |  |  |  |  |  | 5 | 3
2 | If the program cannot train new members in a timely fashion, then our critical path will be affected |  |  |  |  |  |  | 5 | 3
10 | If Elon Musk changes critical rules that harms our access to Twitter (now X), then our mission success criteria regarding sending tweets may be affected |  |  |  |  |  |  | 3 | 3
11 | If mentors are unavailable to assist with major decisions and tasks, then our critical path may be affected |  |  |  |  |  |  | 3 | 3
3 | If we cannot acquire facilities for building and securing flight hardware, then our delivery may be delayed |  |  |  |  |  |  | 2 | 4
16 | If the flight EPS repair delays the flight build, then the delivery to Nanoracks may be delayed |  |  |  |  |  |  | 2 | 4
17 | If we need to add a secondary Radio path to command off our primary transmitter, then our delivery may be delayed. |  |  |  |  |  |  | 2 | 4
7 | If data takes too long to send, then we will not complete a tweet in a pass |  |  |  |  |  |  | 2 | 3
5 | If certified amateur Radio members are not available at the Ground Station, then links may not be established |  |  |  |  |  |  | 1 | 4
15 | If SilverSat doesn’t meet criteria for amatuer Radio frequency coordination, then our schedule will be delayed. |  |  |  |  |  |  | 2 | 2
6 | If temperature exceeds parts limits, then critical functions may fail |  |  |  |  |  |  | 1 | 3
12 | If proper equipment/facilities cannot be secured for flight I&T testing, then the SilverSat CubeSat may fail Nanoracks testing or in Operations |  |  |  |  |  |  | 1 | 3
8 | If we experience long delays in acquiring parts because of the supply chain shortages, then our delivery may be delayed |  |  |  |  |  |  | 1 | 1
4 | CLOSED: If an expensive component breaks before launch requiring us to replace it, then our delivery may be delayed |  |  |  |  |  |  | 1 | 4
9 | CLOSED: If we cannot meet in person more often, then our critical path will be affected |  |  |  |  |  |  | 1 | 3
13 | CLOSED, COMBINED WITH 12: If proper equipment/facilities cannot be secured for flight I&T testing, then the SilverSat CubeSat may fail in Operations |  |  |  |  |  |  | 1 | 3
14 | CLOSED: If we cannot find a new place to meet, then our critical path will be affected. |  |  |  |  |  |  | 1 | 3
 | 5 |  |  |  |  | 
 | 4 | 5 | 3,16,17 |  |  | 
 | 3 | 6,12 | 7 | 10,11 |  | 1,2
 | 2 |  | 15 |  |  | 
 | 1 | 8 |  |  |  | 
 |  | 1 | 2 | 3 | 4 | 5
 |  | Likelihood (L) |  |  |  | 
Consequence (C)
Slide
Notes: Zoe

## Slide 96: SilverSat Schedule (1 of 4)
Slide

## Slide 97: SilverSat Schedule (2 of 4)
Slide

## Slide 98: SilverSat Schedule (3 of 4)
Slide

## Slide 99: SilverSat Schedule (4 of 4)
Slide

## Slide 100: SilverSat Open Items Update
Attitude Control - Need to conduct detailed design for passive magnetic stabilization
  Open - Have conducted initial simulations only. Need to analyze further, choose magnetic materials, and incorporate into the design
Thermal Design - Need to conduct thermal analysis
  Open - No analysis to date
  Design does not contain anything ‘out of family’ for 1U missions. Expect our thermal profile to be similar.
  Power budget is sensitive to battery heater cycling
Antenna
  Resolved - Using the EnduroSat Antenna. Purchased an EM Antenna for conducting one deployment test, and measure RF return loss.
Spacecraft Telemetry
  Resolved - Implemented RReport command to Avionics
Slide
Notes: Dave

## Slide 101: SilverSat Open Items Update
Flight Model I&T Facilities - Need to secure where we can store flight components, and assemble/test the flight unit
  Open
    Secured facilities in Columbia for PCB population
    Evaluating using the APL STEM facilities for flight build
  Wish to secure facilities for environmental testing, but it is not a requirement for flight
    Nanoracks will facilitate the vibration testing required for score
Ground Station Facilities - Need to secure a location for Ground Station
  Resolved
    Working with Goddard Amateur Radio Club to use their facilities
    Designed Ground Station equipment to be portable
Materials - The camera contains ABS plastic
  Resolved - ABS is an acceptable material for Nanoracks
Slide
Notes: Dave

## Slide 102: Outline
Overview & Mission Concept
Systems Engineering
Preliminary Designs (Major Components)
  Power, Avionics, Radio, Ground, Payload, Mechanical
Prototype 2 Results
FM Integration and Test
Programmatics
Conclusion/Outbrief
Slide

## Slide 103: Conclusion and Thank You!
The SilverSat Team is ready for Flight Build and Test
We would like to thank you, the Reviewers, for your time and your feedback
We would also like to thank those individuals and organizations that have supported our efforts to date
  AGI, Inc
  The Maryland Space Business Roundtable
  Rockville MakerSpace
  Steve Morris, Catylator, LLC.
  Nanoracks
  NASA CSLI Partners
SilverSat Limited logo designed by Brent Almond, Designer Daddy
Slide
Notes: Zoe

## Slide 104: Questions?
Slide

## Slide 105: Review Board Outbrief
How did the CDR go?
Do you have any comments or suggestions for us?
Do you have any action items for us?
Slide

## Slide 106: Backup Slides
Slide

## Slide 107: SilverSat Risk Matrix - Likelihood Criteria
Type ¦¦ Rank | 1 | 2 | 3 | 4 | 5
Technical - estimated likelihood of not meeting mission requirements (educating) | 0-15% | 16-25% | 26-50% | 51-75% | >75%
Cost - estimated likelihood of exceeding available funds | 0-5% | 6-10% | 11-25% | 26-50% | >50%
Schedule - estimated likelihood of missing delivery date | 0-15% | 16-25% | 26-50% | 51-75% | >75%
Slide
Notes: Zoe

## Slide 108: SilverSat Risk Matrix - Consequence Criteria*
Type ¦¦ Rank | 1 | 2 | 3 | 4 | 5
Technical | No impact to full mission success criteria | Minor impact to full mission success criteria | Moderate impact to full mission success criteria. Minimum mission success criteria are achievable with margin | Major impact to full mission success criteria. Minimum mission success criteria are achievable | Minimum mission success criteria are not achievable
Cost | <2% increase over allocated and negligible impact on reserve | Between 2% and 5% increase over allocated and can handle with reserve | Between 5% and 7% increase over allocated and cannot handle with reserve | Between 7% and 10% increase over allocated and/or exceeds proper reserves | >10% increase over allocated and/or cannot handle with reserve
Schedule | No or negligible slip in schedule | Slip in schedule that does not impact critical path/delivery | Slip in schedule that does impact critical path/delivery, but can be mitigated with schedule reserve | Slip in schedule that does impact critical path/delivery and cannot be mitigated with schedule reserve; slip to delivery = 1-3 months | Slip in schedule that does impact critical path/delivery and cannot be mitigated with schedule reserve; slip to delivery = >3 months
* Criteria are based on GSFC-STD-0002
Slide
Notes: Zoe

## Slide 109
AX5043 “Shield”
Flatsat
Wireless Access Point (or phone)
-96dB
FTDI cable
RPi 4
Adafruit Metro M0
Ser1
Ser0
Radio Debug Serial
Nom. Pout ~15dBm
Can configure through SW to about 0 dBm (est.)
Nom. rcvd pwr ~ -67 to -97 dBm
Nom. Pout +29dBm
Nom rcvd pwr ~ -96 to -126dBm (assuming 0 dBm out from Dev platform)
Leakage pwr est ~ -50dBm (80dB), shielded box effectiveness needs to be on order of 80-90 dB. (leakage needs to be at or below noise floor, not sensitivity)
“Ground station” PC
Expected receiver sensitivity between -110 and -120dBm
Total attenuation required 115 to 125dB.
Shielded enclosure required to complete testing (in fully assembled configuration)
Link is not symmetric; we’re testing FlatSat Rx, so its okay that we are not at noise floor of Ground Station Radio
Dev platform
Test Ground Station Hardware (Simplified)
Laptop
RPi (debug logging)
Radio Debug Serial
109
Slide
Notes: Aidan

## Slide 110
Parameter | Value
Modulation (data mode) | GMSK (h=0.5)
Data encoding | NRZI
Deviation | +/- 2.4 kHz (h=0.5)
Transmit BW | 28.8 KHz (main lobe) (19.2kbaud), 14.4 KHz (9600 baud)
Symbol rate (BITRATE) with FEC | 19.2kbps
Symbol rate (BITRATE) without FEC | 9600 bps
FEC | Uncoded, or Rate 1/2 , k=7 Convolutional
Operating frequency range | 400 to 520 MHz
Operating frequency | TBD
Receiver Bandwidth | 14400 Hz (9600) 28800 Hz (19200)
Error control | TBD
Radio Serial1 settings | 19200, N, 8, 1
Radio Serial0 settings | 57600, N, 8, 1
Radio Communication Characteristics
Slide

## Slide 111: What Way are We Pointing?
CS
ANTENNA
Z-axis
“The Antenna is positioned at the origin of the coordinate system hence the Antenna boresight (θ =0 deg and φ =0 deg) is along the Z axis on the top cover of the Antenna.”
So, if the camera is pointed down, then we’re LHCP
Slide

## Slide 112: Top-Level Diagram
From PA
To Rx
From LNA
To Outside Switch
Inside Segment
Outside Segment
PA needs 13.8V @ 13A, N-connector in/out.
Is there an interface on PA? PTT?
Add lightning arrestors at entry
Need to think about lightning protection here too
GS Transceiver PCB
GROUND
PROXY
Cable
Power Amplifier
Cable
Cable
Cable
To Filter
Driver Amplifier
Power Supply
Slide

## Slide 113
* Student code used for Morse Code Generation
Slide
Important points:
Single threaded, non-blocking to max extent possible
Sets up and manages Radio
Continually polls interfaces (Serial0, Serial1, SPI)
No flow control. BIG buffers
Transmit/Receive state must be changed by software
Performs clear channel assessment, transmits when clear
Processes cmds, executes if local, forwards if remote
Fast frequency updates for doppler compensation
Prototype Radio Code Main Loop
(Mentor Version*)
Poll Interfaces
Command Processor
TX
State?
Process packet
Cmd buff
Data buff
Exec Cmd
Remote
CMD
Local
CMD
CCA
RX state
TX
State
RTS?
pkt rcvd?
Forward to endpoint
N
Y
N
Y
N
N
Y
TX
Buff empty
?
TX
Busy?
Tx Pkt
Process cmd buffer
Y
Process data buffer
Arrows indicate main loop in idle state
Notes: Isaac using Tom's script below.
The radio processor has two serial interfaces. Neither interface has flow control. Incoming data is buffered. Only complete packets are processed..
The transceiver (AX5043) is connected to the processor via the SPI bus. The radio has two states, transmit and receive. It must be commanded into the appropriate state by the processor. The transceiver idles in the receive state.
Incoming serial packets are KISS encoded. This is used to delimit packets in the buffers. The KISS address byte is used to determine local commands versus remote commands intended for the satellite.
Packets intended to be transmitted are KISS decoded to guarantee a fixed maximum length. Radio (over-the-air) packets are HDLC encoded by the AX5043.
AVIONICS commands are limited to ASCII characters, so we don’t have to remove KISS encoding. Local commands are executed immediately.
While waiting for data to arrive, the code follows the arrows.
It first polls the serial interfaces, and if there is data in the buffers it is processed.
Command packets intended for the local radio are immediately executed, otherwise they are transferred into the data buffer.
If the radio is in the transmit state, it begins sending out packets to the radio. The radio has a separate FIFO that can hold one packet at a time.
In the receive state, the radio is polled to see if a packet has arrived. Received packets are KISS encoded and forwarded to the appropriate serial interface.
A clear channel is determined by the CCA block. The transmit state can only be entered when the receiver is idle, the channel is clear, and if there is something to send. Packets in the data buffer are transmitted when the channel is clear.
When the transmit buffer is empty, the radio reverts to the receive state.

## Slide 114: Radio Design Decisions
Payload talks directly to the Radio when tweeting
No AX.25. Opted for tncattach over kissattach to reduce per packet overhead
No layer 2 protocol, just TCP. No HW flow control
  We rely on big buffers and TCP to handle end to end flow and error control
Test Ground Station is assumed to be a duplicate of the Satellite Radio, without PA (see Ground Station section)
Doppler compensation only on ground (none on satellite)
Doppler offsets provided by Ground Station software
  Radio can re-tune quickly within expected doppler offset range (AX5043 supports FHSS)
  Ground Station forwards offset to center frequency through local commands to Radio
    Radio retunes up/down depending on TX/RX state and sign of offset
Slide